## Slide 1: Garnet: The Next Generation CGRA Architecture
Priyanka Raina
April 26, 2019

## Slide 2: Challenges with Jade CGRA
1. PE supports only simple integer operations
  Porting applications that use floating point requires application expertise and manual effort

## Slide 3: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
3 3 convolution
Multi-channel 3 3 convolution
Input
K of these
Line Buffer
Double Buffer

## Slide 4: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
Multi-channel 3 3 convolution
K of these
1. Bring in tiles of inputs and weights into local memory reuse them as much as you can
2. Use a double buffer to overlap compute on current tile and fetching of next tile
3. Use a hierarchy of double buffers to maximize energy-efficiency

## Slide 5: Challenges with Jade CGRA
Configuration over JTAG is slow
  Large applications with multiple kernels don’t fit on the CGRA – need fast reconfiguration

## Slide 6: Key (application driven!) architectural changes in Garnet CGRA
Support for Bfloat16, and for executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks, and double buffer support in all memories
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 7: CGRA
 | Processing Element
 | (PE) / Compute
 | Memory (MEM)
 | Switch box (SB)
 | Connection box (CB)
MEM
MEM
MEM
MEM
PE
PE
PE
PE
PE
PE
PE
PE
MEM
MEM
MEM
MEM
Coarse Grained Reconfigurable Array (CGRA)
Tile

## Slide 8: Interconnect
Keyi Zhang

## Slide 9: Connection Box (CB)
PE
CB
10 vertical 16 bit tracks
5 driven up, 5 driven down
10 horizontal 16 bit tracks
5 driven left, 5 driven right
10-to-1 mux
A
B
There are similar 1 bit CBs for feeding 1 bit inputs from 10 horizontal and vertical 1 bit tracks
CB
SB

## Slide 10: Switch Box (SB)
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Pipeline register
PE

## Slide 11: Switch Box (SB)
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Figure shows connectivity for ‘0’ tracks
Similar connectivity for all other numbered tracks
PE output goes to all muxes
PE

## Slide 12: Processing Element
Nikhil Bhagdikar

## Slide 13: Processing Element (PE)
RegA
A
RegB
B
Two 16 bit operands
RegC
D
RegD
E
Three 1 bit operands
RegE
F
8 entry
1 bit look-up table
result
ALU
Add
Mult
And
…
flag

## Slide 14: Diablo vs Lassen
Diablo Ops
Add
Sub
Abs
GTE_Max
LTE_Min
Sel
Mult0
Mult1
Mult2
SHR
SHL
Or
And
XOr
New Ops in Lassen
FPAdd
FPMult
FGetMant
FAddIExp
FSubExp
FCnvExp2F
FGetFInt
FGetFFrac
Lassen supports 16 bit Bfloat type
  1 b sign, 8 b exponent, 7 bit mantissa
  Same range as Float32
Bfloat add and multiply natively
Complex ops like divide, exp, power, log, sin, cos using multiple PE and memory tiles
Allows easy porting of applications!
Enables new applications that need a large range like DNN training or complex ops like divide

## Slide 15: Complex Op Example
Draw the DAG for divide

## Slide 16: Memory
Max Strange

## Slide 17: Memory
In Jade memory tile there are some direct connections (not going through the CBs and SBs to chain line buffers)?
Two single port memory banks
FIFO Controller
Line Buffer Controller
Double Buffer Controller
SRAM
This figure needs more detail!

## Slide 18: Global Buffer
Taeyoung Kong

## Slide 19: Highly banked and configurable global buffer
0 | 1 | 2 | 3 | 4 | 
16 x 32 CGRA
28 | 29 | 30 | 31
…
Address Generation Logic
32 SRAM banks
4 MB total
64 bit wide
64 bit registers
Global Buffer
8 I/O tiles
64b
0
1
2
3
…
4
28
29
30
31
din
addr
addr
dout
Configurable in modes, number of types, capacity, bandwidth for different data
…
…
I/O tile

## Slide 20: Highly banked and configurable global buffer
0 | 1 | 2 | 3 | 4 | 
16 x 32 CGRA
28 | 29 | 30 | 31
…
Address Generation Logic
32 SRAM banks
4 MB total
64 bit wide
64 bit registers
Global Buffer
8 I/O tiles
64b
0
1
2
3
…
4
28
29
30
31
din
addr
addr
dout
Configurable in modes, number of types, capacity, bandwidth for different data
…
…
I/O tile
Config
Weights
Inputs

## Slide 21: Global Buffer – SoC interface
0 | 1 | 2 |  | 31
CGRA appears as an SRAM to the SoC
There is a wrapper that converts this interface into AXI which has block transfers
  Block = 256 words
  Word = 64 bits
  There is an AXI interface for read and another for write
  SoC makes sure that reads and write don’t go to the same bank
wdata (64b)
waddr
wen
raddr
ren
rdata (64b)
Address Decoders
To/from SoC

## Slide 22: Global Buffer – CGRA Interface
To CGRA, we send out data and valid
  Based on start_addr and num_words
From CGRA, we get data and valid

## Slide 23: Configuration through Global Buffer
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | 28 | 29 | 30 | 31
32 CGRA Columns
32 SRAM Banks
8 I/O Tiles
Configuration Bus
{32b config_addr,
32b config_data}
Configuration Bus from Global Controller
Global Address
Decode Logic
Generates rden, addr
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | 28 | 29 | 30 | 31
data

## Slide 24: Global Controller
Alex Carsello

## Slide 25: Configuration Read and Write
How does configuration write and read

## Slide 26: Test and Debug Support
Can read and write all state in the CGRA through JTAG

## Slide 27: Global Signal Tree
Hierarchically connect groups of four tiles with OR gates
MEM
MEM
MEM
MEM
PE
PE
PE
PE
PE
PE
PE
PE
MEM
MEM
MEM
MEM

## Slide 28: Clock Gating Logic

## Slide 29: Power Domains
Ankita Nayak

## Slide 31: Summary of Garnet architectural features
Support for Bfloat16, and for executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 32: SoC
CGRA
Global Buffer
DMA Engine
DMA Engine
TLX
CoreLink
Control Processor
(ARM Cortex M3)
Nested Vector Interrupt Controller (NVIC)
Wake-up Interrupt Controller (WIC)
Memory Protection Unit (MPU)
I-Bus
D-Bus
Debug JTAG
TLX
DRAM
DRAM Controller
Application Processor
FPGA
SRAM
4 Banks
AXI
AXI
AXI
AXI
AHB
AHB
AHB
SoC