## Slide 1: Garnet: The Next Generation CGRA Architecture
Priyanka Raina
April 26, 2019

## Slide 2: Challenges with Jade CGRA
1. PE supports only simple integer operations
  Porting applications that use floating point requires application expertise and manual effort

## Slide 3: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
3 3 convolution
Multi-channel 3 3 convolution
Input
K of these
Line Buffer
Double Buffer

## Slide 4: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
Multi-channel 3 3 convolution
K of these
1. Bring in tiles of inputs and weights into local memory reuse them as much as you can
2. Use a double buffer to overlap compute on current tile and fetching of next tile
3. Use a hierarchy of double buffers to maximize energy-efficiency

## Slide 5: Challenges with Jade CGRA
Configuration over JTAG is slow
  Large applications with multiple kernels don’t fit on the CGRA – need fast reconfiguration

## Slide 6: Key (application driven!) architectural changes in Garnet CGRA
Support for Bfloat16, and for executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks, and double buffer support in all memories
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 7: CGRA
 | Processing Element
 | (PE) / Compute
 | Memory (MEM)
 | Switch box (SB)
 | Connection box (CB)
MEM
MEM
MEM
MEM
PE
PE
PE
PE
PE
PE
PE
PE
MEM
MEM
MEM
MEM
Coarse Grained Reconfigurable Array (CGRA)
Tile

## Slide 8: Interconnect
Keyi Zhang

## Slide 9: Connection Box (CB)
PE
CB
10 vertical 16 bit tracks
5 driven up, 5 driven down
10 horizontal 16 bit tracks
5 driven left, 5 driven right
10-to-1 mux
A
B
There are similar 1 bit CBs for feeding 1 bit inputs from 10 horizontal and vertical 1 bit tracks
CB
SB

## Slide 10: Switch Box (SB)
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Pipeline register
PE

## Slide 11: Switch Box (SB)
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Figure shows connectivity for ‘0’ tracks
Similar connectivity for all other numbered tracks
PE output goes to all muxes
PE

## Slide 12: Processing Element
Nikhil Bhagdikar

## Slide 13: Processing Element (PE)
RegA
A
RegB
B
Two 16 bit operands
RegC
D
RegD
E
Three 1 bit operands
RegE
F
8 entry
1 bit look-up table
result
ALU
Add
Mult
And
…
flag

## Slide 14: Diablo vs Lassen
Diablo Ops
Add
Sub
Abs
GTE_Max
LTE_Min
Sel
Mult0
Mult1
Mult2
SHR
SHL
Or
And
XOr
New Ops in Lassen
FPAdd
FPMult
FGetMant
FAddIExp
FSubExp
FCnvExp2F
FGetFInt
FGetFFrac
Lassen supports 16 bit Bfloat type
  1 b sign, 8 b exponent, 7 bit mantissa
  Same range as Float32
Bfloat add and multiply natively
Complex ops like divide, exp, power, log, sin, cos using multiple PE and memory tiles
Allows easy porting of applications!
Enables new applications that need a large range like DNN training or complex ops like divide

## Slide 15: Complex Op Example
Draw the DAG for divide

## Slide 16: Memory
Max Strange

## Slide 17: Memory
In Jade memory tile there are some direct connections (not going through the CBs and SBs to chain line buffers)?
Two single port memory banks
FIFO Controller
Line Buffer Controller
Double Buffer Controller
SRAM
This figure needs more detail!

## Slide 18: Global Buffer
Taeyoung Kong

## Slide 19: Global Buffer – Main Functions
Highly banked buffer for data reuse
Buffer to store bitstream for parallel reconfiguration
=> Design Philosophy: Make global buffer simple and flexible

## Slide 20: Global Buffer – Components
Global Buffer
64b
0
1
2
3
28
29
30
31
…
32 SRAM banks
4 MB total
64 bit wide
Bank Array
AXI – bank Interconnect
8 I/O controller + controller<->bank interconnect
I/O controller_0
I/O controller_7
I/O controller_1
I/O controller_6
…
8 config controller + controller<->bank interconnect
Config controller_0
Config controller_7
Config controller_1
Config controller_6
…

## Slide 21: Global Buffer – SoC interface
0 | 1 | 2 |  | 31
CGRA appears as a Memory to the SoC
SoC provides a wrapper that converts between this simple interface into AXI interface which has block transfers
  Block = 256 words * 64 bits/word
Pipelined to support high clock frequency
wdata (64b)
waddr
wen
raddr
ren
rdata (64b)
Address Decoders
To/from SoC

## Slide 22: Global Buffer – I/O controller
0 | 1 | 2 | 3 | 4 | 
16 x 32 CGRA
28 | 29 | 30 | 31
Global Buffer
64b
0
1
2
3
…
4
28
29
30
31
din
addr
addr
dout
Configurable in modes, number of types, capacity for different data
…
…
I/O controller_0
I/O controller_7
Weights
Inputs

## Slide 23: Global Buffer – I/O controller
To CGRA, we send out data and valid
From CGRA, we get data and valid
Start_addr
Addr
Num_word
Addr
Gen
Ren
16b Data
Valid
64b Data
Addr
Addr
Gen
Ren
16b Data
Valid
64b Data
<FIFO mode>
<SRAM mode>
Addr_high
Addr_low
Ren

## Slide 24: Global Buffer – Parallel Reconfiguration
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | 28 | 29 | 30 | 31
32 CGRA Columns
32 SRAM Banks
8 config controllers
Configuration Bus
{config_write,
32b config_addr,
32b config_data}
Configuration Bus from Global Controller
Global Address
Decode Logic
Generates rden, addr
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | 28 | 29 | 30 | 31
data
…
…

## Slide 25: Global Controller
Taeyoung Kong & Alex Carsello

## Slide 26: Configuration – AXI4-Lite & JTAG
JTAG is able to write/read to CGRA configuration and TOP configuration
AXI4-Lite is able to write to TOP configuration
Global
controller
tck
tdi
trst
tms
tdo
wr_en
wr_addr[15:0]
wr_data[31:0]
rd_addr[15:0]
rd_data[31:0]
rd_en
interrupt
JTAG
AXI4-Lite
wrapper
Global buffer
Parallel Config Controller
CGRA
configuration
bus
TOP configuration bus

## Slide 27: CGRA control – start & done
Block level of application is controlled by cgra_start and cgra_done
Global
controller
Global buffer
I/O controller
cgra_start_pulse
cgra_done_pulse
Input
data
output
data
Input
data

## Slide 28: Global Signal Flow
<River-flowing input>
PE
PE
PE
PE
Global signals
(clk, reset, config_wr)
PE
PE
PE
PE
PE
PE
PE
32’h0
PE
PE
PE
32’h0
Config_read_data
<River-flowing output>

## Slide 29: Debug Support by JTAG
JTAG can do everything!
Debug CGRA fabric
  Write/read CGRA-configuration registers
  Write/read SRAM in CGRA fabric
  4bit stall signal
    Every tile has configuration registers to select a stall signal from 4bits
Debug CGRA fabric + global buffer
  Write/read TOP-configuration registers
  Write/read SRAM in global buffer
  Write/read CGRA control register (cgra_start)

## Slide 30: Power Domains
Ankita Nayak

## Slide 31: Motivation
Adoption of ‘Design for PPA’ mindset
Save power by turning off tiles in the fabric not actively used

## Slide 32: Architectural Features
1. Power Switch Network Architecture
2. Boundary protection between
the active and shutdown tiles
3. FT to connect IO near shutdown logic to the active part & for global signals

## Slide 33: ON-OFF Boundary Protection
2. Use the existing muxes in the design
for boundary protection
1. Redesign the muxes in the design to allow for inherent clamping mechanism
AON : Always ON
SD : Shutdown

## Slide 34: Tile Architecture
PS
PS
PS
PS
PS
PS
PS
PS
PS
PS
PS
PS
AON
SD
Configuration register and its decode logic for enabling the power switches is kept ON
Buffers and logic on global signals are kept ON
All other logic is shutdown when the tile is turned OFF
GLOBAL SIGNAL BUFFERS
DECODE LOGIC
PS EN

## Slide 35: Top Level – Different sections can be turned ON/OFF by P&R

## Slide 36: Summary of Garnet architectural features
Support for Bfloat16, and for executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 37: SoC
CGRA
Global Buffer
DMA Engine
DMA Engine
TLX
CoreLink
Control Processor
(ARM Cortex M3)
Nested Vector Interrupt Controller (NVIC)
Wake-up Interrupt Controller (WIC)
Memory Protection Unit (MPU)
I-Bus
D-Bus
Debug JTAG
TLX
DRAM
DRAM Controller
Application Processor
FPGA
SRAM
4 Banks
AXI
AXI
AXI
AXI
AHB
AHB
AHB
SoC